## Slide 1: Data center environment
Notes: Module – 2
Data Center Environment

## Slide 2
Upon completion of this module, you should be able to:
  Describe the core elements of a data center
  Describe virtualization at application and host layer
  Describe disk drive components and performance
  Describe host access to storage through DAS
  Describe working and benefits of flash drives
Data Center Environment

## Slide 3: Data Center Environment
During this lesson the following topics are covered:
  Application and application virtualization
  DBMS
  Components of host system
  Compute and memory virtualization
Application, DBMS, and Host (Compute)

## Slide 4: Application
A software program that provides logic for computing operations
Commonly deployed applications in a data center:
  Business applications – email, enterprise resource planning (ERP), decision support system (DSS)
  Management applications – resource management, performance tuning, virtualization
  Data protection applications – backup, replication
  Security applications – authentication, antivirus
Key I/O characteristics of an application
  Read intensive vs. write intensive
  Sequential vs. random
  I/O request size

## Slide 5: Application Virtualization
Allows application to be delivered in an isolated environment
  Aggregates Operating System (OS) resources and the application into a virtualized container
  Ensures integrity of Operating System (OS) and applications
  Avoids conflicts between different applications or different versions of the same application
It is the technique of presenting an application to an end user without any installation, integration, or dependencies on the underlying computing platform.
Application Virtualization

## Slide 6: Database Management System (DBMS)
Database is a structured way to store data in logically organized tables that are interrelated
  Helps to optimize the storage and retrieval of data
DBMS controls the creation, maintenance, and use of databases
  Processes an application’s request for data
  Instructs the OS to retrieve the appropriate data from storage
Popular DBMS examples are MySQL, Oracle RDBMS, SQL Server, etc.

## Slide 7: Host (Compute)
Resource that runs applications with the help of underlying computing components
  Example: Servers, mainframes, laptop, desktops, tablets, server clusters, etc.
Consists of hardware and software components
Hardware components
  Include CPU, memory, and input/output (I/O) devices
Software components
  Include OS, device driver, file system, volume manager, and so on
IP

## Slide 8: Operating Systems and Device Driver
In a traditional environment OS resides between the applications and the hardware
  Responsible for controlling the environment
In a virtualized environment virtualization layer works between OS and hardware
  Virtualization layer controls the environment
  OS works as a guest and only controls the application environment
  In some implementation OS is modified to communicate with virtualization layer
Device driver is a software that enables the OS to recognize the specific device

## Slide 9: Memory Virtualization
An OS feature that presents larger memory to the application than physically available
  Additional memory space comes from disk storage
  Space used on the disk for virtual memory is called ‘swap space/swap file or page file’
  Inactive memory pages are moved from physical memory to the swap file
  Provides efficient use of available physical memory
  Data access from swap file is slower – use of flash drives for swap space gives best performance
Operating System
Memory
Swap in
Swap out
Disk Drive

## Slide 10: Logical Volume Manager (LVM)
Responsible for creating and controlling host level logical storage
  Physical view of storage is converted to a logical view
  Logical data blocks are mapped to physical data blocks
One or more Physical Volumes form a Volume Group
  LVM manages Volume Groups as a single entity
Logical volumes are created from the volume group
Logical Disk Block
Volume Group
Physical Vol. 2
Physical Vol. 3
Logical Volume
Logical Volume
Physical Vol. 1

## Slide 11: LVM Example: Partitioning and Concatenation
Partitioning
Concatenation
Logical Volume
Physical Volume
Hosts

## Slide 12: File System
1
2
3
4
5
6
Mapped to
Mapped to
Users
Files
File System
File System Blocks
LVM Logical Extents
Disk Physical
Extents
Disk Sectors
Creates/
Manages
Mapped to
Reside in
Mapped to

## Slide 13: Compute Virtualization
Enables creation of multiple virtual machines (VMs), each running an OS and application
  VM is a logical entity that looks and behaves like physical machine
Virtualization layer resides between hardware and VMs
  Also known as hypervisor
VMs are provided with standardized hardware resources
It is a technique of masking or abstracting the physical compute hardware and enabling multiple operating systems (OSs) to run concurrently on a single or clustered physical machine(s).
Compute Virtualization
CPU
Memory
NIC Card
Hard Disk
Virtualization Layer (Hypervisor)
x86 Architecture

## Slide 14: Need for Compute Virtualization
Before Virtualization | After Virtualization
Runs single operating system (OS) per machine at a time Couples s/w and h/w tightly May create conflicts when multiple applications run on the same machine Underutilizes resources Is inflexible and expensive | Runs multiple operating systems (OSs) per physical machine concurrently Makes OS and applications h/w independent Isolates VM from each other, hence, no conflict Improves resource utilization Offers flexible infrastructure at low cost
x86 Architecture
CPU
Memory
NIC Card
Hard Disk
CPU
Memory
NIC Card
Hard Disk
Virtualization Layer (Hypervisor)
x86 Architecture

## Slide 15: Desktop Virtualization
Enables organizations to host and centrally manage desktops
  Desktops run as virtual machines within the data center and accessed over a network
Desktop virtualization benefits
  Flexibility of access due to enablement of thin clients
  Improved data security
  Simplified data backup and PC maintenance
It is a technology which enables detachment of the user state, the Operating System (OS), and the applications from endpoint devices.
Desktop Virtualization
LAN/WAN
Desktop VMs
Pcs and thin clients

## Slide 16: Connectivity
The following points are covered in this topic:
  Physical components of connectivity
  Storage connectivity protocols

## Slide 17: Connectivity
Interconnection between hosts or between a host and peripheral devices, such as storage
Physical Components of Connectivity are:
  Host interface card, port, and cable
Protocol = a defined format for communication between sending and receiving devices
  Popular storage interface protocols: IDE/ATA and SCSI
Host
Adapter
Port
Cable
Disk

## Slide 18: IDE/ATA and Serial ATA
Integrated Device Electronics (IDE)/Advanced Technology Attachment (ATA)
  Popular interface used to connect hard disks or CD-ROM drives
  Available with varity of standards and names
Serial Advanced Technology Attachment (SATA)
  Serial version of the IDE/ATA specification that has replaced the parallel ATA
  Inexpensive storage interconnect, typically used for internal connectivity
  Provides data transfer rate up to 6 Gb/s (standard 3.0)

## Slide 19: SCSI and SAS
Parallel Small computer system interface (SCSI)
  Popular standard for connecting host and peripheral devices
    Commonly used for storage connectivity in servers
  Higher cost than IDE/ATA, therefore not popular in PC environments
  Available in wide variety of related technologies and standards
  Support up to 16 devices on a single bus
  Ultra-640 version provides data transfer speed up to 640 MB/s
Serial Attached SCSI (SAS)
  Point-to-point serial protocol replacing parallel SCSI
  Supports data transfer rate up to 6 Gb/s (SAS 2.0)

## Slide 20: Fibre Channel and IP
Fibre Channel (FC)
  Widely used protocol for high speed communication to the storage device
  Provides a serial data transmission that operates over copper wire and/or optical fiber
  Latest version of the FC interface ‘16FC’ allows transmission of data up to 16 Gb/s
Internet Protocol (IP)
  Traditionally used to transfer host-to-host traffic
  Provide opportunity to leverage existing IP based network for storage communication
    Examples: iSCSI and FCIP protocols

## Slide 21
During this topics following points are covered:
  Various storage options
Storage

## Slide 22: Storage Options
Magnetic Tape
  Low cost solution for long term data storage
    Preferred option for backup destination in the past
  Limitations
    Sequential data access
    Single application access at a time
    Physical wear and tear
    Storage/retrieval overheads

## Slide 23: Storage Options (contd.)
Optical discs
  Popularly used as distribution medium in small, single-user computing environments
  Limited in capacity and speed
  Write once and read many (WORM): CD-ROM, DVD-ROM
  Other variations: CD-RW, Blu-ray discs
Disk drive
  Most popular storage medium
  Large storage capacity
  Random read/write access
Flash drives
  Uses semiconductor media
  Provide high performance and low power consumption

## Slide 24
Disk drive Components

## Slide 26
Disk drive Performance

## Slide 27
Seek Time

## Slide 28
Seek Time
Disk vendors publish the following seek time specifications:
Full Stroke: time taken by the R/W head to move across the entire width of the disk, from the innermost track to the outermost track.
Average:The average time taken by the R/W head to move from one random track to another,
normally listed as the time for one-third of a full stroke.
Track-to-Track: time taken by the R/W head to move between adjacent tracks

## Slide 29
Disc Transfer Rate

## Slide 30
Host Access to Storage
Data is accessed and stored by applications using the underlying infrastructure.

## Slide 31
Direct Attached Storage(DAS)
DAS is an architecture in which storage is connected directly to the hosts.
Ex. The internal disk drive of a host and the directly connected external storage array
  DAS is classified as
  internal or
  external,
based on the location of the storage device

## Slide 32: Module 1: ch2 Data Center Environment
  VMware ESXi
Concept in Practice

## Slide 33: VMware ESXi
Industry’s leading hypervisor
  Enable virtualization of x86 hardware platforms
Physical machine that houses ESXi is called ESXi host
  ESXi host abstracts physical compute resources to run multiple VMs concurrently on same physical server
Two Components
  VMKernel
    Work similar to OS – responsible for process creation, resource scheduling, and so on
  Virtual machine monitor
    Performs binary translation for privileged OS instructions that can not be virtualized

## Slide 34: Summary
Key points covered in this module:
Key data center elements
Application and compute virtualization